## Slide 1
How To: Record uterine artery Doppler pulsatility index (PI) at 11+0 to 13+6 weeks’ gestation
Indication: To screen in the first trimester for pre-eclampsia and/or fetal growth restriction
Machine settings: Routine first-trimester scan preset with color Doppler velocity 30–40 cm/s, pulsed wave Doppler velocity 80–100 cm/s, low filter (50–100 Hz) and pulsed Doppler sample volume 2 mm
“How To” record uterine artery Doppler at 11–13 weeks

## Slide 2
Uterine artery Doppler: identifying the cervix
Obtain a mid-sagittal section of the uterus and cervix
Use HD zoom to enlarge the view of the cervix

## Slide 3
Uterine artery Doppler: identifying the uterine artery
Apply color flow mapping
Slide the transducer to view the para-cervical region
Gently move the transducer from side to side to identify the uterine artery
The uterine arteries are at the level of the internal cervical os
Mid-sagittal view
Paramedian view
Bladder
Cervix

## Slide 4
Uterine artery Doppler: obtaining a spectral Doppler signal
Set the sampling gate to 2 mm so as to cover whole vessel
Angle of insonation should be less than 30º
The peak systolic velocity should be more than 60 cm/s in the uterine artery
Obtain three similar consecutive waveforms
The mean PI is obtained as the average of the left PI and right PI
Color Doppler of uterine arteries
Uterine artery waveform